## Slide 1
The CGRA generator implements N global signals. N is a generator parameter with the default value of four.
The global signal network consists of a “combination” part, and a “distribution” part. The combination part muxes global signal sources, while the distribution part distributes the muxed signal to every PE/Mem tile in the CGRA.
The distribution part is implemented as N hierarchical high fanout trees. Each PE/Mem tile receives these N inputs. These global inputs can be used as data (they are connected to connection boxes) and/or they can be used to clock gate a tile. Each tile has a CB feature that can be used to gate the tile’s clock.
Continued on next slide
PE/Mem Tile
GST Tile
A
B
C
Global Signal Architecture

## Slide 2
PE Tile
The combination part is implemented as a pyramid. Each PE/Mem tile has a 1-bit global output signal, which is connected to the 1-bit PE output. If present, multiple 1-bit PE outputs are muxed to generate a single 1-bit output. This mux appears as a “feature” in the PE tile config space, and can be programmed accordingly. The global output signals of four adjacent PE/Mem tiles are muxed in a new type of tile (global signal tile or GST) to generate a single output (eg: C). The outputs of four adjacent GST tiles are muxed again in a GST (eg: B). This process continues till all PE/Mem tiles are connected to GSTs, and all GSTs are connected through one top level GST (A).
This particular implementation of the combinational part limits the number of sources in a network quad to one due to GST output contention (a GST tile has 4 inputs, but only 1 output)
Global Signal Architecture
1 Bit Connection Box
Regular
Fabric
Routing
Wires
Global
Wires
Global wires can be used as data inputs
as they are connected to ALU’s CBs
Ungated Clock
1 Bit Connection Box
Regular
Fabric
Routing
Wires
Global
Wires
Global wires can be used for clock gating
enable
Gated clock
used by rest of the PE/Mem Tile

## Slide 3
GST Architecture
GST tile muxes signals from lower level tiles (lower level = closer to the PE/Mem tiles), and buffers global signals from higher level GST tiles and passes them to the lower level tiles.
It creates a hierarchical global signal network by muxing the outputs to the lower level. Any of the GST outputs can be used to distribute either the higher level signal or one of the GST inputs from the lower level. A GST tile effectively “controls” the global signals for lower level tiles. This relation is reflected in the cgra_info.txt as follows -
0x559 is the tile address of the parent tile, while 0x540, 0x541, 0x549, and 0x548 are the tile address of the child (or controlled) tiles. This information is useful, for example, for gating only a part of the CGRA fabric.
GST tiles can be configured like any PE/Mem tile using the tile/feature addresses specified in the cgra_info.txt.
GST Tile
Inputs from lower level PE/Mem/GST Tiles. Each lower level tile contributes one input.
Higher level GST
Outputs to lower level PE/Mem/GST Tiles. All N signals are connected to each lower level tile.
<tile type='gst' tile_addr='0x559'>
<controlled_tiles>
<tile>0x540</tile>
<tile>0x541</tile>
<tile>0x549</tile>
<tile>0x548</tile>
</controlled_tiles>
</tile>
Distribution
Combination